## Slide 1
AVR Timer Waveform Generation Documentation
Project Overview :
This project generates four distinct waveforms using AVR microcontroller timers (Timer0, Timer1, Timer2) at 8 MHz CPU clock. Timer0 produces a CTC square wave on PB3, Timer1 generates dual Fast PWM signals on PD5/PD4, and Timer2 creates Phase Correct PWM on PD7. All use 1024 prescaler for precise frequency control matching embedded timing applications.
System Architecture
Timer Block Diagram :
AVR Microcontroller (8 MHz)
├── Timer0 (CTC) → OC0 (PB3) Square Wave ~97.66 Hz
├── Timer1 (Fast PWM 8-bit) → OC1A (PD5), OC1B (PD4) PWM ~30.52 Hz
└── Timer2 (Phase Correct PWM) → OC2 (PD7) PWM ~15.32 Hz
Prescaler: 1024 for all timers

## Slide 2
Timer | Mode | WGM Bits | TOP | OCR Value | Output Pin(s) | COM Bits
Timer0 | CTC | WGM01=1 | OCR0 | 80 | PB3 (OC0) | COM00=1 (Toggle) smart-home-documentation.pdf​
Timer1 | Fast PWM 8-bit | WGM10=1 | 255 | OCR1A=64, OCR1B=64 | PD5, PD4 | COM1A1:0=2, COM1B1:0=2 smart-home-documentation.pdf​
Timer2 | Phase Correct PWM | WGM20=1 | 255 | 64 | PD7 (OC2) | COM21:20=2 (Clear Up/Set Down) smart-home-documentation.pdf​
Timer Configurations :

## Slide 3
Waveform Generation Details :
Timer0 CTC Waveform
Frequency Calculation: Timer clock = 8MHz/1024 = 7812.5 Hz Tick time = 1/7812.5 = 0.128 ms Period = 2 × OCR0 × tick_time = 2 × 80 × 0.128 ms = 20.48 ms Frequency = 1/20.48 ms = 97.66 Hz​
Timer1 Fast PWM
Frequency Calculation: Period = 256 × 0.128 ms = 32.768 ms Frequency = 30.52 Hz (25% duty cycle at OCR=64)​
Timer2 Phase Correct PWM
Frequency Calculation: Period = 2 × 255 × 0.128 ms = 65.28 ms Frequency = 15.32 Hz (25% duty cycle at OCR2=64)​
Function Implementations
TIMER0_CTC_wave_nonpwm()
- TCCR0 = (1<<WGM01) | (1<<CS02) | (1<<CS00); // CTC, Prescaler 1024
- OCR0 = 80; // Compare match value
- TCCR0 |= (1<<COM00); // Toggle OC0 on compare

## Slide 4
TIMER1_fast_pwm_8bit_wave()
- TCCR1A = (1<<WGM10); // Fast PWM 8-bit
- TCCR1B = (1<<CS12) | (1<<CS10); // Prescaler 1024
- OCR1A = OCR1B = 64; // 25% duty cycle
- TCCR1A |= (1<<COM1A1)|(1<<COM1B1); // Clear/Set OC1A/OC1B
TIMER2_phase_correct_pwm_wave()
- TCCR2 = (1<<WGM20) | (1<<COM21) | (1<<CS22) | (1<<CS20); // Phase PWM, Prescaler 1024
- OCR2 = 64; // Duty cycle control
Key Concepts :
CTC Mode: Clears timer on compare match, toggles output for square wave generation.
Fast PWM: Fixed TOP=255, frequency independent of duty cycle, ideal for motor control.
Phase Correct PWM: Counts up/down to TOP, symmetrical waveform reduces harmonic distortion.
Prescaler Impact: 1024 divides 8MHz to 7.8125kHz tick rate, balancing resolution and range.​
Practical Applications
Motor Control: PWM duty cycle controls speed/torque
LED Dimming: Variable brightness via duty cycle
Audio Generation: CTC square waves for tones
Servo Control: Precise PWM pulse widths
Signal Generation: Custom frequency waveforms for sensors/comms

## Slide 5
Testing Validation :
Test Case | Configuration | Expected Output | Pass Criteria
TC-01 | Timer0 OCR0=80 | PB3 toggles @97.66Hz | Oscilloscope verification smart-home-documentation.pdf​
TC-02 | Timer1 OCR1A=64 | PD5/PD4 PWM 30.52Hz, 25% duty | Duty cycle measurement
TC-03 | Timer2 OCR2=64 | PD7 symmetric PWM 15.32Hz | Waveform symmetry check smart-home-documentation.pdf​